## Slide 1
SMALLHOLDER IRRIGATION PRODUCTIVITY FOR SUSTAINABLE INTENSIFICATION: WATER BALANCES FOR HIGH VALUE CROPS IN NORTHERN GHANA
Adimassu et al.
International Water Management Institute (IWMI)

## Slide 2: Introduction
Sustainable intensification for smallholder farming systems in sub-humid and semiarid zones of West Africa critically hinges not only on agronomy and crop varieties but also the management of agricultural water to enhance crop and livestock productivities especially in the dry season
Efficiency of water in agricultural production is generally low at field /farm level in Northern Ghana
Understanding the dry spell length and its impact on productivity is crucial to develop agricultural water management strategies with smallholder framers to attain production and productivity gains.
Moreover, dry season irrigation systems are crucial for sustainable intensification in the Region
Objective
  Explore incidence of dry spell occurrence and the impacts on major commodities, such as maize, in rainfed systems.
  Explore opportunity in dry season irrigation systems for vegetables and the implications on water balances and water productivity of different water management strategies

## Slide 3: Research approach
Historical daily climate data including rainfall were obtained from meteorological stations in northern Ghana
Long term dry spell analysis was carried out using INSTAT+ v3.37
Dry spell length and the probabilities of dry spell lengths exceeding 7, 10, 14 and 21 days were calculated for each of the 10 stations in northern Ghana
The output from this was then extrapolated over northern Ghana to create maps of dry spell probabilities of the area using ArcGIS and PCRaster
CROPWAT 8.0 was used to
  Calculate crop water requirement for wet and dry season crops
  Estimate yield reduction at different rainfall regimes and soil types for maize during wet season
  Irrigation requirement for dry season crops and simulate supplementary irrigation for wet season maize during sever dry spell

## Slide 4: Results and discussion
There is a 60-80% chance of a dry spell exceeding 7 days and 30-40% chance of a dry spell exceeding 10 days
Dry spells ultimately resulting in yield decrease unless water management strategies are.
Shorter dry spells (7 -10 days) can be overcome by infield water harvesting and increasing water holding capacity of the soils,
However for longer dry spells (14-21 days) supplementary irrigation is to be considered.
Chart: Water deficit (mm)
| Normal rainfall | 25% above the normal rainfal | 25% below the normal rainfall | Normal rainfall | 25% above the normal rainfal | 25% below the normal rainfall | Normal rainfall | 25% above the normal rainfal | 25% below the normal rainfall | Clay loam | Loam | Sandy loam
Water deficient (mm) | 37.5 | 0 | 152 | 0 | 0 | 205.8 | 25 | 0 | 151.9
Yield reduction (%) | 0 | 0 | 21.4 | 0 | 0 | 18.6 | 0 | 0 | 25.4
When rainfall below 25% of the normal rainfall is observed, significant yield reduction of maize is expected in all soil types. This implies the need for strategies related to agricultural water management options such as supplementary irrigation

## Slide 5: Results and Discussion
Dry season irrigation results in best productivity (kg yield m-3 water applied) between 50-75% of crop requirement, resulting in yields, 70-90% of potential yield if well scheduled for typical high value crops such as tomato, onion and pepper.
Chart: Time of application
| Optimum irrigation | 25% depletion | 40% depletion | 50% depletion | 75% depletion
Clay loam soil | 7.9098 | 6.856 | 7.7422 | 7.2339 | 10.1524
Loam soil | 7.4808 | 7.5721 | 8.0484 | 8.4503 | 13.4805
Sandy loam soil | 7.2754 | 6.9055 | 7.1474 | 7.2334 | 6.7245
Chart: Time of application
| Optimum irrigation | 25% depletion | 40% depletion | 50% depletion | 75% depletion
TNI (mm)_Clay loam | 505.7 | 577.6 | 496.5 | 514.8 | 301.8
TNI (mm)_Loam | 534.7 | 523.5 | 479.1 | 438.8 | 217.5
TNI (mm)_Sandy loam | 549.8 | 572.3 | 533.9 | 508.2 | 426.5
YR (%)_Clay loam | 0 | 1 | 3.9 | 6.9 | 23.4
YR (%)_Loam | 0 | 0.9 | 3.6 | 7.3 | 26.7
YR (%)_Sandy loam | 0 | 1.2 | 4.6 | 8.1 | 28.3
The highest yield reduction of tomato at all levels of soil moisture depletion were observed in sandy loam soils due to the low total available soil moisture
The lowest yield reduction were observed in clay loam soils

## Slide 6: Conclusion
Dry spells within the growing season is affecting crop yields,
  For example, during the long dry spell, maize yield can reduce up to 25%. This requires up to 150 mm supplementary irrigation during the dry spells.
Full irrigation is typically not water productive, but an application between 50-75% of water potential yields 70-90% of potential yield if well scheduled for typical high value crops such as tomato, onion and pepper.
To maximize incomes per unit water in dry season irrigation, farmers need good scheduling advice and –or devices.
This also benefits sustainable intensification as water productivity is higher under 50-75 % of maximum crop water requirement
Hence we recommend to assist farmers in technologies and approaches to enhance infiltration and root depth to bridge natural variable rainfall, promote accessible water management technologies and scheduling to maximize water benefits in dry season irrigation.